## Slide 1: Testbed for Surface Detection with Ultrasound Responsible Professor : Univ.-Prof. Dr.-Ing. Giovanni Del Galdo Supervisors : Dr.-Ing Florian Roemer, M.Sc. Eduardo Perez Mejia

## Slide 2: Ultrasound NDT Setup
Robotic Positioning System
Controlling position and angle
Measurement Collection
Detection of surface
Transducer
Specimen

## Slide 3: Measurement Setup
Signal strength is angle dependent
Better surface detection
Finding optimum orientation

## Slide 4: Motivation
No feedback from positioning system
Latency in measurement collection
Slow calibration testing
Dependency on hardware

## Slide 5: Introduction
Faster prototyping of calibration methods
Removal of hardware dependency
Virtual Calibration Platform
Virtual Measurement setup
Calibration Algorithms
Ray Tracing Model
Stochastic Approximation

## Slide 6: Introduction
Emulate measurement operation.
Stochastic Approximation performs calibration.
Independent sections working together.
Ray Tracer Model
Stochastic Approximation
Geometry
Transducer model
Configuration
Initialize virtual setup
Initialize algorithms
Execution
Measurement data (A - Scan)
Input arguments (x, y, z coordinates of measurement point)

## Slide 7: Ray tracer : Introduction
Ray Tracer : Overview
Assumptions
Building Blocks
Transducer
Frequency of operation
Medium is homogeneous
Wavefields as rays
Convex shape objects
Pulse shaper
Transducer :
Pin hole camera model
Specimen objects
Pulse Shaper:
Choice of pulse shape
Modulation of carrier
Advantages
Simplifies Wave propagation
Less computational cost
Faster measurements.

## Slide 8: Stochastic Approximation : Introduction
Fewer measurements compared to current approach
Automate calibration process
Performance can be optimized
Maximize ?
Function itself is unknown.
Only few measurements are available.
Estimate parameters in less time and high accuracy.

## Slide 9: Stochastic Approximation : Introduction
Methods are iterative
Gradient is approximated
Parameter is updated according to the gradient
Process above is repeated until convergence
Estimated parameter and true solution are compared
Initial guess
Function evaluation
Gradient approximation
Update Parameter

## Slide 10: Ray Tracer Model
Transducer :
  Imaging Plane depicts sensor area
  Plane is discretized into pixels
  Wavefields impinging are treated as rays
  Each pixel is associated with a ray
Imaging Plane
focus

## Slide 11: Ray Tracer Model
Rays shot are checked for intersection
Angle of arrival at defect and transducer
is normal of the plane and is the direction of a ray
Each ray carries a time-of-flight
Source
Surface
Transmitted ray
Reflected ray
is based on angle of arrival at surface and is based on angle of arrival at transducer.
is the total contribution of all rays generated over sensor area.

## Slide 12: Ray Tracer Model
Specimen Object :
  Required to simulate measurement operation
  Planes are used to build a specimen
  Orientation of object is unknown

## Slide 13: Ray Tracer
Pulse Shaper :
  Choice of transmit pulse is often not programmable
  Set of pulse shapes are implemented
  Parameters of each pulse are programmable
  Calibration performance is tested with each pulse shape
Parameter | Value
Bandwidth Factor | 0.7e13
Sampling Frequency | 40 MHz
Center Frequency | 3 MHz

## Slide 14: Pulse Shaper
Carrier with frequency is modulated with a time shifted copies of pulse shape
is the noise and is the total field

## Slide 15: Stochastic Approximation
Methods are analysed based on following factors
  Function evaluations per Iteration
  Computational Complexity
  Factors affecting convergence behaviour
  Stability of algorithm
  Accuracy : Difference between estimated and true solution
Performance optimization
Inter algorithm performance comparison
Algorithms use the virtual data

## Slide 16: Stochastic Approximation : Stochastic Gradient Ascent
Stochastic Gradient Ascent :
Parameter update equation :
is the approximated gradient and is the estimated parameter vector
Function evaluations increase with parameters
Parameters | Details
Function Evaluations per Iteration | For number of parameters function evaluations
Factors affecting convergence | Step size mainly decides the rate of convergence
Parameters | Details
Function Evaluations per Iteration | 
Factors affecting convergence | 

## Slide 17: Stochastic Approximation : Stochastic Gradient Ascent
Effect of Step size on Convergence
Different Step sizes are configured
Parameter | Values
SNR | 20 dB
Initial guess azimuth | 0
Initial guess elevation | 0
Iterations | 30

## Slide 18: Stochastic Approximation : Variants of Gradient Ascent
Variants of Gradient Ascent :
  Gradient Ascent with Momentum :
Update eqation :
Momentum is kept between to
Oscillations are produced
Parameters | Details
Function Evaluations per Iteration | For parameters, function evaluations.
Factors affecting convergence | Momentum factor and Step size
Parameters | Details
Function Evaluations per Iteration | 
Factors affecting convergence | 

## Slide 19: Stochastic Approximation : Variants of Gradient Ascent
Momentum factor on Convergence behavior.
Faster convergence
Oscillations produced for high momentum
Parameter | Values
SNR | 20 dB
Step size | 0.05
Initial guess azimuth | 0
Initial guess elevation | 0
Iterations | 30

## Slide 20: Stochastic Approximation : Variants of Gradient Ascent
  Accelerated Gradient Ascent:
Update equation :
Correction factor reduces oscillations
Parameters | Details
Function Evaluations per Iteration | For parameters, function evaluations.
Factors affecting convergence | Correction factor, Momentum factor and Step size
Parameters | Details
Function Evaluations per Iteration | 
Factors affecting convergence | 

## Slide 21: Stochastic Approximation : Variants of Gradient Ascent
Important to observe the effect of correction factor.
Reduced oscillations
Correction factor important for high momentum values
Parameter | Values
SNR | 20 dB
Step size | 0.05
Initial guess azimuth | 0
Initial guess elevation | 0
Iterations | 30

## Slide 22: Stochastic Approximation : SPSA
Simultaneous Perturbation Stochastic Approximation:
Update equation :
Adaptive step size : .
Suitable for large number of parameters.
Parameters | Details
Function Evaluations per Iteration | Only 2 function evaluations, irrespective of number of parameter being optimized.
Factors affecting convergence | Step size mainly affects the rate of convergence. It uses adaptive step size.
Parameters | Details
Function Evaluations per Iteration | Only 2 function evaluations, irrespective of number of parameter being optimized.
Factors affecting convergence | 
Parameter | Value
Initial guess azimuth | 0
Initial guess elevation | 0
Iterations | 30

## Slide 23: Stochastic Approximation : SPSA
Stability of Algorithm is tested

## Slide 24: Stochastic Approximation : Algorithm Performance Comparison
Test scenario is configured
Performance Comparison
  Iterations required
  Function evaluations
  Accuracy
  Stability
Suitability for real world testing
Parameter | Values
SNR | 20 dB
Step size | 0.05
Initial guess azimuth | 0
Initial guess elevation | 0
Iterations | 30
Test Scenario

## Slide 25: Stochastic Approximation : Algorithm Performance Comparison

## Slide 26: Algorithm Performance Comparison : Summary
Performance analysis
Experiment is run for 30 Iterations.
 | Function Evaluations/Iteration | Total Function Evaluations
Gradient Ascent | 4 | 120
Gradient Ascent with momentum | 4 | 120
Accelerated Gradient Ascent | 4 | 120
SPSA | 2 | 60
Newton’s Method | 9 | 270
Quasi Newton’s Method | 4 | 120
For Current experiment

## Slide 27: Summary and Contribution
Virtual Calibration Platform
Useful prior to real world testing
Faster prototyping
Removal of hardware dependency
Programmability of Parameters
Automation of Calibration process

## Slide 28: Conclusion
Alternative to hardware-based calibration
Independent Components working together
Automation of calibration
Optimization of performance
Limitations of measurement model

## Slide 29: Thank you !!!
Questions

## Slide 30: Extra Slides

## Slide 31: Problem Description
Goal is to identify and localize defects.
Strength of reflected signal is angle dependent.
Transmit pulse must be shot at an optimum angle.
Robotic Positioner (Holding Transducer)
Surface under test
Position and orientation of transducer is controlled.
Transmit Pulse
Reflected Signal
https://link.springer.com/chapter/10.1007/978-3-642-32261-7_5
Reflectivity is angle dependent

## Slide 32: Ray Tracer Model
Rays shot from focus travel through the center of each pixel into 3D space.
Direction of each ray is given by the pixel coordinates and focus.
is the direction, is the source and defines how far away the ray has travelled.
is the focus kept behind at a distance from the center of the plane.
is the center, is the focal length and is the normal of the plane.

## Slide 33: Problem Description
Finding an optimum angle is calibration of positioning system.
Performed before measurement campaign.
Fully hardware dependent.
Calibration of positioning system
Manual calibration
Stochastic Approximation
Taking measurements at each possible angle and calculating energy.
Starting with an initial guess of and letting the algorithm run to find optimum angle.

## Slide 34: SPSA

## Slide 35: Stochastic Approximation : Newton’s Method
Newton’s Method :
Update equation :
is the hessian matrix
approximated with finite difference approximation
Sensitive to initial guess of parameter
Parameters | Details
Function Evaluations per Iteration | For current application 9 function evaluations are required.
Factors affecting convergence | The initial guess is often chosen closer to the true solution

## Slide 36: Stochastic Approximation : Newton’s Method
Sensitivity to initial guess is tested
Sensitive to initial guess
Possibility of divergence
Parameter | Value
Step size | 0.05
SNR | 20 dB
Iterations | 30

## Slide 37: Stochastic Approximation : Quasi Newton’s Method
Quasi Newton’s Method :
Hessian matrix is only updated.
Saves number of function evaluations.
Update equation :
is updated in each iteration.
Parameter | Details
Function Evaluations per Iteration | Same as Gradient Ascent
Factors affecting convergence | Scaling factor used while initialization of hessian matrix with an identity matrix.

## Slide 38: Stochastic Approximation : Quasi Newton’s Method
Using different scaling factors algorithm is tested
Increase in scaling factor reduces rate of convergence
Parameter | Value
SNR | 20 dB
Step size | 0.05
Initial guess azimuth | 0
Initial guess elevation | 0
Iterations | 30

## Slide 39: SPSA 20 dB animation

## Slide 40: Calibration Framework
Combines ray tracer and calibration algorithms.
Programmability of parameters and Less dependency on Hardware.
Faster testing of calibration methods.
Calibration Framework
Ray Tracer Model
Calibration Algorithms
Initialize hardware setup
Configure transducer parameters.
Take the measurement based on input arguments
Initialize algorithm parameters
Use the measurement interface with required set of arguments
Collect and process measurement.
Input arguments
Amplitude Scan